SEA HYDRAULIC RAM SERVICE SCHEDULE

This service schedule is not intended to cover every aspect of a site service but should assist the engineer in his work and act as a useful aid memoir.

(Tick relevant boxes or fill-in/delete as required)

General Condition of the operators

Flexible Cable(s)          Rear brackets & swivel pins      Front bracket & swivel/ball joint(s)

Good	      Replace          Good        Replace                           Good        Replace

OIL

Any visible sign of oil leaks?  No        Yes      If yes, where

Check/top-up oil levels with operators in open position.  Top up req. yes/no.  Oil changed

N.B. The oil should be changed every 2-3 years on normally operated residential applications and at least every year on intensively used sites.

Operation – Are the rams running:-

Smoothly	             Quietly                Speed (single ram)    Speed (when operating as a pair)

Yes       No                Yes       No         OK      Slow                 OK      Out - which ram?

STOPS

Check open & close physical ground stops are present - Stops OK            Attention req.

Emergency Release; Functioning correctly?                     Mini/Mark Tank key type

Yes          No                    Key No.                      Older Hexagon        Blue Robot Head

Operator Pressures

Check the open & close pressure settings:  Pressures OK        Pressures Adjusted

Locking – Check hydraulic locking by leaving the gate(s) against stops for 10 minutes minimum

Electric locks and cables should be inspected, adjusted as required and lubricated

Locking OK                   Attention required        To what?_____________________

Lubricate

Ram swivel points         Gate hinges        Grease exposed piston rod (gate in open position)

Please turn over

SAFETY, SECURITY and ELECTRICAL

CRUSH/PINCH POINTS

IMPORTANT: The EU Machinery Directive 97/38EC is now in force.  Automatic gate systems are require to have devices to be fitted to them to prevent injury by crushing, pinching or striking.

Operate and check the system for possible crush or pinch points.

Check that any operating/start devices, for example Push buttons, Key or Digital Switch can not be reached and operated by putting a hand/arm through the gate(s). If they can it is dangerous; Change or disable immediately.

If a crush/pinch point is identified, a ‘Safety Device’ should be recommended and installed to prevent any accidents occurring.

Suitable ‘Safety Devices’ include; Safety Edges and the ‘Safety Gate’. More information on these and other products can be obtained from SEA (UK) Ltd; the telephone number is shown at the foot of this page.

Crush Inspection Check OK          Attention needed        To what?

Photocells

N.B. Two sets of Photocells are recommended to provide satisfactory vehicle safety:

One set of Photocells should be fitted on the inside of the gate(s) - just past the opening arc of the gate(s). And a second set on the outside of the gate(s) just past the gate(s) closed line.

Location of the photocells:

Inside & outside the gate(s)         Outside the gate(s) only        Inside the gate(s) only

Check the Photocells operation & condition     OK         Attention needed

Loop Detector. Check any Induction Loop(s) fitted is/are working as intended. If a Loop is fitted to provide ‘hold open’ safety, park a vehicle on the loop to check it will hold for a sufficient amount of time.

Loop(s) OK                 Attention needed         To what?

Start Devices

Check all ‘start’ devices work correctly i.e. Radio Tx, Push Buttons, Digital Switch etc.

Start devices OK             In need of attention          Which one?

Electrical: Visually check the entire system for any faults or potential faults and infestation.

Electrical Inspection        OK               Attention needed        To what?

Test the RCD and local ‘Isolation Switch’

RCD/Switch Test OK                  Attention needed         To what?

Notes and comments:

SEA UK Ltd - Tel: 0121 706 9629 - Fax: 0121 764 5603 – Email: sales@seaukltd.co.uk

# Text boxes

Model			Type of ram 		Stroke (mm)		Type of internal Locking

Mini Tank		  -   			270			SC	SA	AC	SB

Mark Tank		  -			270			SC	SA	AC	SB

Half Tank  		100  200 		270  390 	SC	SA	AC	SB

Full Tank		100  200 	270  390 	SC	SA	AC	SB